Christian Manalo Mañibo - isx9565961
1. Utilitza el Packet Tracer per construir la xarxa que us especifica el següent Diagrama de Topologia. Utilitza els routers 1841 i configura'ls per tal que tinguin 2 ports serial.

Crea la Taula d'Adreçament corresponent a aquest Diagrama de Topologia.

	Nom del Dispositiu	Interfície (IP + MX)	Gateway
Xarxa 1 (LAN1) / 172.16.3.0/24	R1	172.16.3.1 255.255.255.0	172.16.3.1
	Servidor DHCP	172.16.3.2 255.255.255.0	172.16.3.1
	PC1	Automatic	172.16.3.1
	PC2	Automatic	172.16.3.1
Xarxa 2 (LAN2) / 172.16.1.0/24	R2	172.16.1.1 255.255.255.0	172.16.1.1
	Servidor DHCP	172.16.1.2 255.255.255.0	172.16.1.1
	PC1	Automatic	172.16.1.1
	PC2	Automatic	172.16.1.1
Xarxa 3 (LAN3) / 192.168.2.0/24	R3	192.168.2.1 255.255.255.0	192.168.2.0
	Servidor DHCP	192.168.2.2 255.255.255.0	192.168.2.0
	PC1	Automatic	192.168.2.0
	PC2	Automatic	192.168.2.0
Xarxa 4 (WAN1) / 172.16.2.0/24	R1	172.16.2.1 / 255.255.255.0	172.16.2.1
	R2	172.16.2.2 / 255.255.255.0	172.16.2.2
Xarxa 5 (WAN2) / 192.168.1.0/24	R2	192.168.1.2 / 255.255.255.0	192.168.1.2
	R3	192.168.1.1 / 255.255.255.0	192.168.1.1

1. Configureu, per CLI (línia de comandes)
Les adreces IP dels routers
Router1
Router>enable / Router#configure term / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#interface fa0/0 / Router(config-if)#ip address 172.16.3.1 255.255.255.0 / Router(config-if)#no shutdown / Router(config-if)#interface s0/0/0 / Router(config-if)#ip address 172.16.2.1 255.255.255.0 / Router(config-if)#no shutdown / Router(config-if)#exit

Router 2
Router>enable / Router#configure term / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#interface fa0/0 / Router(config-if)#ip address 172.16.1.1 255.255.255.0 / Router(config-if)#no shutdown / Router(config-if)#interface s0/0/0 / Router(config-if)#ip address 172.16.2.2 255.255.255.0 / Router(config-if)#no shutdown / Router(config-if)#interface s1/0/0 / Router(config-if)#ip address 192.168.1.2 255.255.255.0 / Router(config-if)#no shutdown / Router(config-if)#exit

Router 3

Router>enable / Router#configure term / Enter configuration commands, one per line. End with CNTL/Z. / Router(config)#interface fa0/0 / Router(config-if)#ip address 192.168.2.1 255.255.255.0 / Router(config-if)#no shutdown / Router(config-if)#interface s1/0/0 / Router(config-if)#ip address 192.168.1.1 255.255.255.0 / Router(config-if)#no shutdown / Router(config-if)#exit

Les adreces dels PCs, mitjançant DHCP
Copia la configuració del running-config a l'startup-config. No t'oblidis d'anar fent aquest pas a mesura que avances en l'exercici.
Router 1
Router#show running-config / Building configuration... / Current configuration : 854 bytes / ! / version 12.4 / no service timestamps log datetime msec / no service timestamps debug datetime msec / no service password-encryption / ! / hostname Router / ! / ! / no ip cef / no ipv6 cef / ! / ! / spanning-tree mode pvst / ! / ! / interface FastEthernet0/0 / ip address 172.16.3.1 255.255.255.0 / duplex auto / speed auto / ! / interface FastEthernet0/1 / no ip address / duplex auto / speed auto / shutdown / ! / interface Serial0/0/0 / ip address 172.16.2.1 255.255.255.0 / clock rate 2000000 / ! / interface Serial0/0/1 / no ip address / clock rate 2000000 / shutdown / ! / interface Serial0/1/0 / no ip address / clock rate 2000000 / shutdown / ! / interface Serial0/1/1 / no ip address / clock rate 2000000 / shutdown / ! / interface Vlan1 / no ip address / shutdown / ! / ip classless / ! / ip flow-export version 9 / ! / ! / ! / line con 0 / ! / line aux 0 / ! / line vty 0 4 / login / ! / ! / end

Router 2
Router#copy running-config startup-config / Destination filename [startup-config]? / Building configuration... / [OK] / Router#show running-config / Building configuration... / Current configuration : 847 bytes / ! / version 12.4 / no service timestamps log datetime msec / no service timestamps debug datetime msec / no service password-encryption / ! / hostname Router / ! / ! / no ip cef / no ipv6 cef / ! / ! / spanning-tree mode pvst / ! / ! / interface FastEthernet0/0 / ip address 172.16.1.1 255.255.255.0 / duplex auto / speed auto / ! / interface FastEthernet0/1 / no ip address / duplex auto / speed auto / shutdown / ! / interface Serial0/0/0 / ip address 172.16.2.2 255.255.255.0 / ! / interface Serial0/0/1 / ip address 192.168.1.2 255.255.255.0 / clock rate 2000000 / ! / interface Serial0/1/0 / no ip address / clock rate 2000000 / shutdown / ! / interface Serial0/1/1 / no ip address / clock rate 2000000 / shutdown / ! / interface Vlan1 / no ip address / shutdown / ! / ip classless / ! / ip flow-export version 9 / ! / line con 0 / ! / line aux 0 / ! / line vty 0 4 / login / ! / end

Router 3
Router#copy running-config startup-config / Destination filename [startup-config]? / Building configuration... / [OK] / Router#show ru / Router#show running-config / Building configuration... / Current configuration : 836 bytes / ! / version 12.4 / no service timestamps log datetime msec / no service timestamps debug datetime msec / no service password-encryption / ! / hostname Router / ! / ! / no ip cef / no ipv6 cef / ! / ! / ! / spanning-tree mode pvst / ! / ! / interface FastEthernet0/0 / ip address 192.168.2.1 255.255.255.0 / duplex auto / speed auto / ! / interface FastEthernet0/1 / no ip address / duplex auto / speed auto / shutdown / ! / interface Serial0/0/0 / no ip address / clock rate 2000000 / shutdown / ! / interface Serial0/0/1 / ip address 192.168.1.1 255.255.255.0 / ! / interface Serial0/1/0 / no ip address / clock rate 2000000 / shutdown / ! / interface Serial0/1/1 / no ip address / clock rate 2000000 / shutdown / ! / interface Vlan1 / no ip address / shutdown / ! / ip classless / ! / ip flow-export version 9 / ! / ! / line con 0 / ! / line aux 0 / ! / line vty 0 4 / login / ! / ! / ! / end

Visualitza les taules d'enrutament de cada router i comprova que contenen les xarxes connectades directament a cadascun d'ells. Quina comanda utilitzes per veure la taula d'enrutament d'un router? Inclou el resultat.
R1
Router#show ip route / Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP / D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area / N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2 / E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP / i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area / * - candidate default, U - per-user static route, o - ODR / P - periodic downloaded static route / Gateway of last resort is not set / 172.16.0.0/24 is subnetted, 3 subnets / S 172.16.1.0 [1/0] via 172.16.2.2 / C 172.16.2.0 is directly connected, Serial0/0/0 / C 172.16.3.0 is directly connected, FastEthernet0/0 / S 192.168.2.0/24 [1/0] via 172.16.2.2

R2
Router#show ip route / Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP / D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area / N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2 / E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP / i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area / * - candidate default, U - per-user static route, o - ODR / P - periodic downloaded static route / Gateway of last resort is not set / 172.16.0.0/24 is subnetted, 3 subnets / C 172.16.1.0 is directly connected, FastEthernet0/0 / C 172.16.2.0 is directly connected, Serial0/0/0 / S 172.16.3.0 [1/0] via 172.16.2.1 / C 192.168.1.0/24 is directly connected, Serial0/0/1 / S 192.168.2.0/24 [1/0] via 192.168.1.1

R3
Router#show ip route / Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP / D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area / N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2 / E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP / i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, ia - IS-IS inter area / * - candidate default, U - per-user static route, o - ODR / P - periodic downloaded static route / Gateway of last resort is not set / 172.16.0.0/24 is subnetted, 2 subnets / S 172.16.1.0 [1/0] via 192.168.1.2 / S 172.16.3.0 [1/0] via 192.168.1.2 / C 192.168.1.0/24 is directly connected, Serial0/0/1 / C 192.168.2.0/24 is directly connected, FastEthernet0/0

1. Quin grup de comandes has hagut d'executar per configurar la interfície Fa0/0 del Router R1? Indica també, el «mode» en el que s'ha de trobar el router per tal d'executar cadascuna de les comandes (per exemple: R1#).
  R1> enable
  R1 # config term
  R1 (config) # interface fa0/0
  R1 (config) # ip address 172.16.3.1 255.255.255.0
  R1 (config)# no shutdown
2. Quin grup de comandes has hagut d'executar per configurar el servei DHCP del Router R1 per a la Xarxa 1 (LAN1)? Indica també, el «mode» en el que s'ha de trobar el router per tal d'executar cadascuna de les comandes (per exemple: R1#).
  Lo he configurat graficament perquè encara no ens han ensenyat en el mode de comandes CLI.
3. Activa el «debug» de la taula d'enrutament per als tres routers. És a dir, activa el servei que t'avisa de qualsevol canvi que es produeixi en la taula d'enrutament. Aquest servei s'activa mitjançant la comanda Router#debug ip Routing
  Router#debug ip routing
IP routing debugging is on

Acaba de configurar les taules d'enrutament dels tres routers mitjançant «enrutament estàtic: next-hop» (només rutes per a les LAN). Indica quina comanda has d'executar al router R1 per tal de configurar la ruta estàtica a la xarxa 192.168.2.0/24.

En el mode de simulació del Packet Tracer, envia 3 missatges ping i comprova que tant l'enviament del ping com el retorn de la resposta funcionen.
El primer ping que vagi del PC1 al PC2
C:\>ping 172.16.1.4 / Pinging 172.16.1.4 with 32 bytes of data: / Reply from 172.16.1.4: bytes=32 time=10ms TTL=126 / Reply from 172.16.1.4: bytes=32 time=10ms TTL=126 / Reply from 172.16.1.4: bytes=32 time=10ms TTL=126 / Reply from 172.16.1.4: bytes=32 time=10ms TTL=126

- El segon ping que vagi del PC2 al PC3
C:\>ping 192.168.2.3 / Pinging 192.168.2.3 with 32 bytes of data: / Reply from 192.168.2.3: bytes=32 time=10ms TTL=126 / Reply from 192.168.2.3: bytes=32 time=10ms TTL=126 / Reply from 192.168.2.3: bytes=32 time=10ms TTL=126 / Reply from 192.168.2.3: bytes=32 time=10ms TTL=126

- El tercer pring que vagi del PC3 al PC1
C:\>ping 172.16.1.3 / Pinging 172.16.1.3 with 32 bytes of data: / Request timed out. / Reply from 172.16.1.3: bytes=32 time=1ms TTL=126 / Reply from 172.16.1.3: bytes=32 time=1ms TTL=126 / Reply from 172.16.1.3: bytes=32 time=1ms TTL=126